## Slide 1
Chapter One
Data Communication and Computer Networking Basics

## Slide 2: Objectives
At the end of this Chapter Students should be able to:
  Understand the concept of Network, Data communication
  Know the components of data communication
  Identify the various application of Networks
  Understand the classification of Network

## Slide 3: Cont’d…
  Discuss the different shape of a network with their respective cons and prons.
  Describe the use of Network protocol and their significance
  Know the Network reference model both OSI as well as TCP/IP models

## Slide 4: Introduction
  Old paradigm: a single powerful computer serving all the needs of an organization
  New paradigm† - Computer networks: a large number of separate (autonomous) but internetworked (being able to exchange information) computers doing the job
    Merging of computer and communications technologies – no geographical barrier
    Connection: copper wire, fiber optics, microwaves, infrared, communication satellites, …
Plus new applications: distributed processing (grid and cluster computing, pervasive computing, …), WWW, …

## Slide 5: Introduction
Data communications and networking
  Change the way we do business and the way we live
  Business decisions have to be made more quickly
  Decision depends on immediate access to accurate information
  Business today rely on computer networks and internetworks
  Before get hooked up, we need to know:
    How networks operate
    What types of technologies are available
    Which design best fills which set of needs

## Slide 6: Introduction
  Development of the PC changes a lot in business, industry, science and education.
  Similar revolution is occurring in data communication and networking
    Technologies advances are making it possible for communications links to carry more and faster signals
    Services are evolving to allow the use of this expanded capacity
    For example telephone services extended to have:
      Conference calling
      Call waiting
      Voice mail
      Caller ID

## Slide 7: 1.1 Data Communications
  Communication:
    Means sharing information
      Local (face to face) or remote (over distance)
    Telecommunication
      Telephone, telegraph and television
      Means communication at a distance
      Tele is Greek for far

## Slide 8: Data Communications
  Data:
    Refers to information
      Presented in any form
      Agreed upon by the parties ( creating & using)
  Data communication : is the exchange of data between two devices via some form of transmission medium (wire cable).

## Slide 9: Data Communications
  Communication system made up of a combination of hardware and software
  Effectiveness of data communication system depends on:
    Delivery : The system must deliver data to correct destination. Data received by the indented user only
    Accuracy: The system must deliver data accurately (no change).
      Data changed & uncorrected is unusable

## Slide 10: Data Communications
    Timeliness: The system must deliver data in timely manner
      Data arrived late are useless
      In the same order (video and audio) & without delay (Real time transmission)
    Jitter: Variation in the packet arrival time (uneven quality in the video is the result)

## Slide 11: Data Communications

## Slide 12
1-1 DATA COMMUNICATIONS
Definition:
The term telecommunication means communication at a distance.
The word data refers to information presented in whatever form is agreed upon by the parties creating and using the data.
Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable.
Components of a data communications system
Data Flow
Topics discussed in this section:

## Slide 13
Figure 1.1 Components of a data communication system
  A data communication system is made up of five components

## Slide 14: Components
  Message: the information (data) to be communicated
    Consist of text, numbers, pictures, audio, or video
  Sender: the device that sends the data message
    Computer, workstation, telephone handset, video camera, …
  Receiver: the device that receives the message
    Computer, workstation, telephone handset, television, ….

## Slide 15: Components
  Medium: The physical path by which a message travels from sender to receiver
    twisted pair, coaxial cable, fiber-optic, radio waves

## Slide 16: Components
  Protocol: a set of rules that govern data communications
    An agreement between the communicating devices
    Devices may be connected but not communicating (no protocol)
    Arabic speaker with Japanese speaker

## Slide 17: Data Representation
Text
Audio
Video
Numbers
Images

## Slide 18: Data Representation
Text:
  Sequence of bits (0s or 1s)
  Different sets of patterns to represent text symbols (each set is called: code)
  ASCII: 7 bits (128 symbols)
  common coding system today is:
  Unicode uses: 32 bits to represent a symbol or character in any language
Unicode
(4,294,967,296)

## Slide 19: Data Representation
Numbers:
  Represented by bit patterns
  The number is directly converted to a binary number

## Slide 20: Data Representation
Images:
  Represented by bit patterns
  A matrix of
  Resolution: size of the pixels
  High resolution: more memory is needed
  Each pixel is assigned a bit pattern
    1-bit pattern (black and white dots image)
    2-bit pattern (4 levels of gray)
    RGB (color images)
pixels

## Slide 21: Data Representation
Audio:
  Continuous not discrete
  Change to digital signal
Video:
  Recording or broadcasting of a picture or movie
  Change to digital signal

## Slide 22: Data Flow
Communication between two devices can be:
  Simplex
  Half-Duplex
  Full-Duplex

## Slide 23: Data Flow
Simplex (one way street)
  The communication is unidirectional
  Only one device on a link can transmit; the other can only receive
  Use the entire capacity of the channel to send data
  Example: Keyboards, Monitors
Data

## Slide 24: Data Flow
Half-Duplex (one-lane with two-directional traffic)
  Each station can both transmit and receive, but not at the same time
  When one device is sending, the other can only receive, and vice versa
  The entire capacity of a channel is taken over by the transmitting device
  Example: Walkie-talkies
Data
Data

## Slide 25: Data Flow
Full-Duplex (Duplex) (two-way street)
  Both stations can transmit and receive at same time
  Signals going in either direction sharing the capacity of the link
  Sharing can occur in two ways:
    Link has two physically separate transmission paths
      One for sending and the other for receiving
    The capacity of the channel is divided between signals travelling in both directions
  Example: Telephone network
Data
Data

## Slide 26: Exercise
What mode of data flow the following exhibits shows?
Answer: Full-Duplex
Data
Data

## Slide 27
Figure 1.2 Data flow (simplex, half-duplex, and full-duplex)

## Slide 28: Networks
  Network : A set of devices (nodes) connected by communication links
    Node : computer, printer, …
    Distributed Processing :
      Most networks used it
      Task is divided among multiple computers instead of one single large computer

## Slide 29: Networks
Network Criteria
    Network must meet a certain number of criteria
    The most important of the network criterions are:
      Performance
      Reliability
      Security

## Slide 30: Networks
Performance
  Transit time: A mount of time required for a message to travel from one device to another
  Response time: Elapsed time between an inquiry and a response

## Slide 31: Networks
Performance
  Performance depends on :
    1- Number of users: large number slow response time.
    2- Type of transmission medium: fiber-optic cabling faster than others cables.
    3- Capabilities of the connected hardware: affect both the speed and capacity of transmission.
    4- Efficiency of the software: process data at the sender and receiver and intermediate affects network performance.

## Slide 32: Networks
Performance
  Performance is evaluated by two contradictory networking metrics:
    Throughput (high): a measure of how fast we can actually send data through a network
    Delay (low)

## Slide 33: Networks
Reliability
  Reliability is measured by:
    Frequency of failure
    Recovery time of a network after a failure
    Network’s robustness in a catastrophe: protect by good back up network system

## Slide 34: Networks
Security
  Protecting data from unauthorized access
  Protecting data from damage and development
  Implementing policies and procedures for recovery from breaches and data losses (Recovery plan)

## Slide 35: Networks
Physical Structures:
  Type of connection
    Network: Two or more devices connected through links
    Link: Communication pathway that transfers data from one device two another
    Two devices must be connected in some way to the same link at the same time. Two possible types:
      Point-to-Point
      Multipoint

## Slide 36: Networks
Point-to-Point
  Dedicated link between two devices
  Entire capacity of the link is reserved for transmission between those two devices
  Use an actual length of wire or cable

## Slide 37: Networks
Point-to-Point
  Other options, such as microwave or satellite is possible
  Example: Television remote control

## Slide 38: Networks
Multipoint (multidrop)
  More than two devices share a single link
  Capacity is shared
  Channel is shared either spatially or temporally
    Spatially shared: if devices use link at same time
    Timeshare: if users must take turns

## Slide 39: Digital Transmission of Digital Data
Computers produce binary data
Standards needed to ensure both sender and receiver understands this data
  Coding: language that computers use to represent letters, numbers, and symbols in a message
  Signaling (aka, encoding): language that computers use to represent bits (0 or 1) in electrical voltage
Bits in a message can be send in
  A single wire one after another (Serial transmission)
  Multiple wires simultaneously (Parallel transmission)

## Slide 40
TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect.
The imperfection causes signal impairment.
This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
What is sent is not what is received.
Three causes of impairment are attenuation, distortion, and noise.

## Slide 41
PROTOCOLS
A protocol is synonymous with rule. It consists of a set of rules that govern data communications. It determines what is communicated, how it is communicated and when it is communicated. The key elements of a protocol are syntax, semantics and timing

## Slide 42
Elements of a Protocol
Syntax
  Structure or format of the data
  Indicates how to read the bits - field delineation
Semantics
  Interprets the meaning of the bits
  Knows which fields define what action
Timing
  When data should be sent and what
  Speed at which data should be sent or speed at which it is being received.

## Slide 43: Standards
Importance
  Provide a “fixed” way for hardware and/or software systems (different companies) to communicate
  Help promote competition and decrease the price
Types of Standards
  Formal standards
    Developed by an industry or government standards-making body
  De-facto standards
    Emerge in the marketplace and widely used
    Lack official backing by a standards-making body

## Slide 44: Standardization Processes
Specification
  Developing the nomenclature and identifying the problems to be addressed
Identification of choices
  Identifying solutions to the problems and choose the “optimum” solution
Acceptance
  Defining the solution, getting it recognized by industry so that a uniform solution is accepted

## Slide 45: Major Standards Bodies
ISO (International Organization for Standardization)
  Technical recommendations for data communication interfaces
  Composed of each country’s national standards orgs.
  Based in Geneva, Switzerland (www.iso.ch)
ITU-T (International Telecommunications Union –Telecom Group
  Technical recommendations about telephone, telegraph and data communications interfaces
  Composed of representatives from each country in UN
  Based in Geneva, Switzerland (www.itu.int)

## Slide 46: Major Standards Bodies (Cont.)
ANSI (American National Standards Institute)
  Coordinating organization for US (not a standards- making body)
  www.ansi.org
IEEE (Institute of Electrical and Electronic Engineers)
  Professional society; also develops mostly LAN standards
  standards.ieee.org
IETF (Internet Engineering Task Force)
  Develops Internet standards
  No official membership (anyone welcomes)
  www.ietf.org

## Slide 47: Some Data Comm. Standards
Layer
Common Standards
5. Application layer
HTTP, HTML (Web)
MPEG, H.323 (audio/video)
IMAP, POP (e-mail)
4. Transport layer
TCP (Internet)
SPX (Novell LANs)
3. Network layer
IP (Internet)
IPX (Novell LANs)
2. Data link layer
Ethernet (LAN)
Frame Relay (WAN)
PPP (dial-up via modem for MAN)
1. Physical layer
RS-232c cable (LAN)
Category 5 twisted pair (LAN)
V.92 (56 kbps modem)

## Slide 48: Switching Networks
Long distance transmission is typically done over a network of switched nodes
Nodes not concerned with content of data
End devices are stations
  Computer, terminal, phone, etc.
A collection of nodes and connections is a communications network
Data routed by being switched from node to node

## Slide 49: Nodes
Nodes may connect to other nodes only, or to stations and other nodes
Node to node links usually multiplexed
Network is usually partially connected
  Some redundant connections are desirable for reliability
Two different switching technologies
  Circuit switching
  Packet switching

## Slide 50: Simple Switched Network

## Slide 51: Circuit Switching
Dedicated communication path between two stations
Three phases
  Establish
  Transfer
  Disconnect
Must have switching capacity and channel capacity to establish connection
Must have intelligence to work out routing

## Slide 52: Circuit Switching - Applications
Inefficient
  Channel capacity dedicated for duration of connection
  If no data, capacity wasted
Set up (connection) takes time
Once connected, transfer is transparent
Developed for voice traffic (phone)

## Slide 53: Packet Switching Principles
Circuit switching designed for voice
  Resources dedicated to a particular call
  Much of the time a data connection is idle
  Data rate is fixed
    Both ends must operate at the same rate

## Slide 54: Basic Operation
Data transmitted in small packets
  Typically 1000 octets
  Longer messages split into series of packets
  Each packet contains a portion of user data plus some control info
Control info
  Routing (addressing) info
Packets are received, stored briefly (buffered) and past on to the next node
  Store and forward

## Slide 55: Use of Packets

## Slide 56: Advantages
Line efficiency
  Single node to node link can be shared by many packets over time
  Packets queued and transmitted as fast as possible
Data rate conversion
  Each station connects to the local node at its own speed
  Nodes buffer data if required to equalize rates
Packets are accepted even when network is busy
  Delivery may slow down
Priorities can be used

## Slide 57: Switching Technique
Station breaks long message into packets
Packets sent one at a time to the network
Packets handled in two ways
  Datagram
  Virtual circuit

## Slide 58: Datagram
Each packet treated independently
Packets can take any practical route
Packets may arrive out of order
Packets may go missing
Up to receiver to re-order packets and recover from missing packets

## Slide 59: Virtual Circuit
Preplanned route established before any packets sent
Call request and call accept packets establish connection (handshake)
Each packet contains a virtual circuit identifier instead of destination address
No routing decisions required for each packet
Clear request to drop circuit
Not a dedicated path

## Slide 60: Virtual Circuits v Datagram
Virtual circuits
  Network can provide sequencing and error control
  Packets are forwarded more quickly
    No routing decisions to make
  Less reliable
    Loss of a node looses all circuits through that node
Datagram
  No call setup phase
    Better if few packets
  More flexible
    Routing can be used to avoid congested parts of the network

## Slide 61: Circuit v Packet Switching
Performance
  Propagation delay
  Transmission time
  Node delay

## Slide 62
1-2 NETWORKS
A network is a set of devices (often referred to as nodes) connected by communication links. A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network. A link can be a cable, air, optical fiber, or any medium which can transport a signal carrying information.
Network Criteria
Physical Structures
Categories of Networks
Topics discussed in this section:

## Slide 63
Network Criteria
Performance
  Depends on Network Elements
  Measured in terms of Delay and Throughput
Reliability
  Failure rate of network components
  Measured in terms of availability/robustness
Security
  Data protection against corruption/loss of data due to:
      Errors
      Malicious users

## Slide 64: The Uses of a Network
Simultaneous access to data
  Data files are shared
    Access can be limited
  Shared files stored on a server
  Software can be shared
    Site licenses
    Network versions
    Application servers
Notes: Teaching Tip
Figure 9A.2 on page 342 visually describes the sharing process. It can be helpful to have students open a shared file that you control. Make a change then have the students open it again. Alternatively, share a document and allow your students to write in it. Then demonstrate how the shared document changes.
Spend time discussing why application servers need to be so powerful.

## Slide 65: The Uses of a Network
Shared peripheral device
  Printers and faxes are common shares
  Reduces the cost per user
  Devices can be connected to the network
  Print servers control network printing
    Manage the print queue
Notes: Teaching tip
Figure 9A.4 on page 344 shows a print queue. It can be helpful to demonstrate your classroom queue.

## Slide 66: Sharing Data
File server contains documents used by other computers.

## Slide 67: The Uses of a Network
Personal communication
  Email
    Instantaneous communication
  Conferencing
    Tele conferencing
    Videoconferencing
    Audio-conferencing
    Data-conferencing
  Voice over IP
    Phone communication over network wires
Notes: Teaching tip
It is fun if you can setup a teleconference in your classroom. Students get to learn how to join or create the conference. Additionally, they learn how to participate. Finally, students have fun, especially with shared whiteboards.

## Slide 68: Voice Over IP

## Slide 69: The Uses of a Network
Easier data backup
  Backup copies data to removable media
  Server data backed up in one step
Notes: Insider information
The text describes needing special software to back up data from user drives. However, the backup utility that comes with Windows 2000 and XP is capable of performing this chore.

## Slide 70: Categories of Networks
Network Category depends on its size
Two primary categories
  LAN: Covers area < 2miles
  WAN: Can be worldwide
  MAN: Between LAN & WAN, span 10s of miles

## Slide 71: Local Area Network (LAN)
Privately owned
Links devices in the same office, building, or campus
Simple LAN: 2 PCs & 1 printer in home or office
Size is limited to a few kilometers
Allow resources to be shared (hardware, software, or data)

## Slide 72: Local Area Network (LAN)
An isolated LAN connecting 12 computers to a hub in a closet

## Slide 73: Local Area Network (LAN)
LAN is distinguished by:
  Size (# users of OS, or licensing restrictions)
  Transmission medium (only one type)
  Topology (bus, ring, star)
Data Rates (speed):
  Early: 4 to 16 Mbps
  Today: 100 to 1000 Mbps

## Slide 74: Wide Area Networks (WAN)
Provides long-distance transmission of data over large geographic areas (country, continent, world)

## Slide 75: Wide Area Networks (WAN)
Switched WAN
  Backbone of the Internet
Dialup line point-to-point WAN
  Leased line from a telephone company

## Slide 76: Wide Area Networks (WAN)

## Slide 77: Metropolitan Area Networks (MAN)
Size between LAN and WAN
Inside a town or a city
Example: the part of the telephone company network that can provide a high-speed DSL to the customer

## Slide 78: Interconnection of Networks: Internetworks
Two or more networks connected together

## Slide 79: The Internet
Internet has revolutionized many aspects of our daily lives.
It has affected the way we do business as well as the way we spend our leisure time.
Internet is a communication system that has brought a wealth of information to our fingertips and organized it for our use
An internet is 2 or more networks that can communicate with each other
The Internet is a collaboration of more than hundreds of thousands of interconnected networks

## Slide 80: The Internet
An internet (small i) is two or more networks
Notable internet is called the Internet (hundreds of thousands interconnected networks)
  Private individuals + government agencies + school + research facilities +
  Corporations + libraries in more than 100 countries
This communication system came in 1969
Mid-1960 (ARPA) Advanced Research Projects Agency in (DOD) was interested to connect mainframes in research organizations
1967, ARPA presented its ideas for ARPANET
  Host computer connecting to (IMP) interface message processor.
  Each IMP communicate with other IMP
1969, four nodes (universities) connected via IMPs to form a network
  Software (NCP) Network Control Protocol provided communication between the hosts.
1972, Vint Cerf and Bob Kahn invented (TCP) Transmission Control Protocol
Later TCP was split to (TCP) Transmission Control Protocol and (IP) Internetworking Protocol

## Slide 81: The Internet
Internet Today
  Made of many LANs and WANs
  Every day new networks area added and removed
  Internet services Providers (ISPs) offer services to the end users
    International service providers
    National service providers
    Regional service providers
    Local service providers
Data
rate

## Slide 82: The Internet
Hierarchical organization of the Internet

## Slide 83: Common Network Types
Local Area Network (LAN)
  Contains printers, servers and computers
  Systems are close to each other
  Contained in one office or building
  Organizations often have several LANS
Notes: Teaching tip
Use a real world example to describe an organization with interconnected LANs.

## Slide 84: Common Network Types
Wide Area Networks (WAN)
  Two or more LANs connected
  Over a large geographic area
  Typically use public or leased lines
    Phone lines
    Satellite
  The Internet is a WAN
Notes: Teaching tip
Blockbuster Video uses a WAN to connect it’s stores nationwide. Customers from Pittsburgh may rent videos in Hilton Head. Late fees will even be displayed!

## Slide 85: Hybrid Network Types
Campus Area Networks (CAN)
  A LAN in one large geographic area
  Resources related to the same organization
  Each department shares the LAN

## Slide 86: Hybrid Network Types
Metropolitan Area Network (MAN)
  Large network that connects different organizations
  Shares regional resources
  A network provider sells time
Notes: Teaching tip
An example of a regional resource is a supercomputer. For example, Pittsburgh has the Pittsburgh Super Computing center (www.psc.edu). The various colleges in Pittsburgh connect to the center through a MAN in Pittsburgh.

## Slide 87: Hybrid Network Types
Home Area Network (HAN)
  Small scale network
  Connects computers and entertainment appliances
  Found mainly in the home

## Slide 88: Hybrid Network Types
Personal Area Network (PAN)
  Very small scale network
  Range is less than 2 meters
  Cell phones, PDAs, MP3 players
Notes: Insider information
PAN is very new. Few devices support PAN. High end cell phones include Bluetooth technology. Once the technology matures, Bluetooth will allow the creation of a PAN.

## Slide 89: How Networks Are Structured
Server based network
  Node is any network device
  Servers control what the node accesses
  Users gain access by logging in
  Server is the most important computer
Notes: Teaching tip
Spend a few minutes here discussing password policies. Describe why it is important not to give out a password. Also describe why longer, more complicated passwords are important.

## Slide 90: How Networks Are Structured
Client/Server network
  Nodes and servers share data roles
  Nodes are called clients
  Servers are used to control access
  Database software
    Access to data controlled by server
  Server is the most important computer

## Slide 91: How Networks Are Structured
Peer to peer networks (P2PN)
  All nodes are equal
  Nodes access resources on other nodes
  Each node controls its own resources
  Most modern OS allow P2PN
  Distributing computing is a form
  Kazaa
Notes: Teaching tip
Discuss how users managing their own security settings can be bad.

## Slide 92: Physical Topology

## Slide 93: Physical Topology
Mesh
  Every link is dedicated point-to-point link
  The term dedicated means that the link carries traffic only between the two devices it connects

## Slide 94: Physical Topology
Mesh
  To link n devices fully connected mesh has: n ( n - 1) / 2 physical channels (Full-Duplex)
  Every Device on the network must have n - 1 ports

## Slide 95: Physical Topology
Mesh
  Example:
  8 devices in mesh has links: n(n-1) / 2
  number of links = 8 (8-1)/2 = 28
  number of ports per device = n – 1 = 8 –1 = 7

## Slide 96: Physical Topology
Mesh
  Advantages
    Each connection carry its own data load (no traffic problems)
    A mesh topology is robust
    Privacy or security
    Fault identification and fault isolation

## Slide 97: Physical Topology
Mesh:
  Disadvantages
    Big amount of cabling
    Big number of I/O ports
    Installation and reconnection are difficult
    Sheer bulk of the wiring can be greater than the available space
    Hardware connect to each I/O could be expensive
Mesh topology is implemented in a limited fashion; e.g., as backbone of hybrid network

## Slide 98: Physical Topology
Star:
  Dedicated point-to-point to a central controller (Hub)
  No direct traffic between devices
  The control acts as an exchange

## Slide 99: Physical Topology
Star
  Advantages
    Less expensive than mesh (1 Link + 1 port per device)
    Easy to install and reconfigure
    Less cabling
    Additions, moves, and deletions required one connection
    Robustness : one fail does not affect others
    Easy fault identification and fault isolation

## Slide 100: Physical Topology
Star
  Disadvantages
    Dependency of the whole topology on one single point (hub)
    More cabling than other topologies ( ring or bus)
Used in LAN

## Slide 101: Physical Topology
Bus
  It is multipoint
  One long cable acts as a backbone
  Used in the design of early LANS, and Ethernet LANs

## Slide 102: Physical Topology
Bus
  Nodes connect to cable by drop lines and taps
  Signal travels along the backbone and some of its energy is transformed to heat
  Limit of number of taps and the distance between taps

## Slide 103: Physical Topology
Bus
  Advantages
    Ease of installation
    Less cables than mesh, star topologies
  Disadvantages
    Difficult reconnection and fault isolation ( limit of taps)
    Adding new device requires modification of backbone
    Fault or break stops all transmission
    The damaged area reflects signals back in the direction of the origin, creating noise in both directions

## Slide 104: Physical Topology
Ring
  Each device has dedicated point-to-point connection with only the two devices on either side of it
  A signal is passed along the ring in one direction from device to device until it reaches its destination
  Each devices incorporates a Repeater

## Slide 105: Physical Topology
Ring
  Advantages
    Easy of install and reconfigure
    Connect to immediate neighbors
    Move two connections for any moving (Add/Delete)
    Easy of fault isolation
  Disadvantage
    Unidirectional
    One broken device can disable the entire network. This weakness can be solved by using a dual ring or a switch capable of closing off the break

## Slide 106: Physical Topology
Hybrid Topology
  Example: having a main star topology with each branch connecting several stations in a bus topology

## Slide 107: Network Topologies
Topology
  Logical layout of wires and equipment
  Choice affects
    Network performance
    Network size
    Network collision detection
  Several different types
Notes: Teaching tip
Discuss how your network topology handles collisions. If your students are technical, contrast this with an inferior topology.

## Slide 108: Network Topologies
Packets
  Pieces of data transmitted over a network
    Packets are created by sending node
    Data is reassembled by receiving node
  Packet header
    Sending and receiving address
  Packet payload
    Number and size of data
    Actual data
  Packet error control
Notes: Teaching tip
For technical students take the time to draw the packet structure on the board. The typical structure is destination address | sending address | packet number | total packets | data size | payload | error control.

## Slide 109: Network Topologies
Bus topology
  Also called linear bus
  One wire connects all nodes
  Terminator ends the wires
  Advantages
    Easy to setup
    Small amount of wire
  Disadvantages
    Slow
    Easy to crash
Notes: Teaching tip
Pages 352 and 353 have diagrams of each network topology

## Slide 110: Network Topologies
Star topology
  All nodes connect to a hub
    Packets sent to hub
    Hub sends packet to destination
  Advantages
    Easy to setup
    One cable can not crash network
  Disadvantages
    One hub crashing downs entire network
    Uses lots of cable
  Most common topology

## Slide 111: Star Topology

## Slide 112: Network Topologies
Ring topology
  Nodes connected in a circle
  Tokens used to transmit data
    Nodes must wait for token to send
  Advantages
    Time to send data is known
    No data collisions
  Disadvantages
    Slow
    Lots of cable

## Slide 113: Network Topologies
Mesh topology
  All computers connected together
  Internet is a mesh network
  Advantage
    Data will always be delivered
  Disadvantages
    Lots of cable
    Hard to setup

## Slide 114: Mesh Topology

## Slide 115: Network Media
Links that connect nodes
Choice impacts
  Speed
  Security
  Size

## Slide 116: Wire Based Media
Twisted-pair cabling
  Most common LAN cable
  Called Cat5 or 100BaseT
  Four pairs of copper cable twisted
  May be shielded from interference
  Speeds range from 1 Mbps to 1,000 Mbps
Notes: Insider information
Interference is usually electrical. Magnets, solar flares or electronic devices generate interference.

## Slide 117: Wire Based Media
Coaxial cable
  Similar to cable TV wire
  One wire runs through cable
  Shielded from interference
  Speeds up to 10 Mbps
  Nearly obsolete

## Slide 118: Wire Based Media
Fiber-optic cable
  Data is transmitted with light pulses
  Glass strand instead of cable
  Immune to interference
  Very secure
  Hard to work with
  Speeds up to 100 Gbps
Notes: Teaching tip
Remind students that bps is bits per second. Gbps then is billion bits per second.

## Slide 119: Wireless Media
Data transmitted through the air
LANs use radio waves
WANs use microwave signals
Easy to setup
Difficult to secure
Notes: Teaching tip
Now is the time to briefly discuss 802.11 standards. A full discussion of 802.11 is covered in the next section.

## Slide 120: Network Hardware
Network interface cards
  Network adapter
  Connects node to the media
  Unique Machine Access Code (MAC)
Notes: Insider Information
The Xerox Corporation controls the assignment of Ethernet addresses to NIC manufacturers.

## Slide 121: Network Hardware
Network linking devices
  Connect nodes in the network
  Cable runs from node to device
  Crossover cable connects two computers

## Slide 122: Network Hardware
Hubs
  Center of a star network
  All nodes receive transmitted packets
  Slow and insecure

## Slide 123: Network Hardware
Switches
  Replacement for hubs
  Only intended node receives transmission
  Fast and secure
Notes: Insider information
Twisted pair networks cannot achieve higher than 10 Mbps using a hub. Switches are necessary to achieve 100 Mbps or higher.

## Slide 124: Network Hardware
Bridge
  Connects two or more LANs together
  Packets sent to remote LAN cross
    Other packets do not cross
  Segments the network on MAC addresses

## Slide 125: Network Hardware
Router
  Connects two or more LANs together
  Packets sent to remote LAN cross
  Network is segmented by IP address
  Connect internal networks to the Internet
  Need configured before installation
Notes: Discussion point
Ask who in the class has high speed Internet. Then determine if anyone is sharing this to the rest of the house or dorm. If they are, see if they can describe the setup. Most likely, the sharing is done with a router.

## Slide 126: Network Hardware
Gateway
  Connects two dissimilar networks
  Connects coax to twisted pair
  Most gateways contained in other devices

## Slide 127: Network Cabling
Cabling specifications
  Bandwidth measures cable speed
    Typically measured in Mbps
  Maximum cable length
  Connector describes the type of plug

## Slide 128: Network Cabling
Ethernet
  Very popular cabling technology
  10 Base T, 10Base2, 10Base5
  Maximum bandwidth 10 Mbps
  Maximum distances100 to 500 meters

## Slide 129: Network Cabling
Fast Ethernet
  Newer version of Ethernet
  Bandwidth is 100 Mbps
  Uses Cat5 or greater cable
    Sometimes called 100Base T
  Requires a switch
Notes: Teaching tip
Point out that the speed of the cable is the number before the word Base.

## Slide 130: Network Cabling
Gigabit Ethernet
  High bandwidth version of Ethernet
  1 to 10 Gbps
  Cat 5 or fiber optic cable
  Video applications

## Slide 131: Network Cabling
Token ring
  Uses shielded twisted pair cabling
  Bandwidth between 10 and 25 Mbps
  Uses a multiple access unit (MAU)
  Popular in manufacturing and finance

## Slide 132: Network Protocols
Language of the network
  Rules of communication
  Error resolution
  Defines collision and collision recovery
  Size of packet
  Naming rules for computers

## Slide 133: Network Protocols
TCP/IP
  Transmission Control Protocol/Internet Protocol
  Most popular protocol
  Machines assigned a name of 4 numbers
    IP address
    209.8.166.179 is the White House’s web site
  Dynamic Host Configuration Protocol
    Simplifies assignment of IP addresses
  Required for Internet access
Notes: Teaching tip
Have students determine IP addresses for the computer. On 2000/XP enter ipconfig /all. Windows 98 and back enter winipcfg.

## Slide 134: Network Protocols
IPX/SPX
  Internet Packet Exchange/Sequenced Packet Exchange
  Older protocol
  Associated with Novell Netware
  Replaced by TCP/IP

## Slide 135: Network Protocols
NetBEUI
  Network BIOS Extended User Interface
  Used by Windows to name computers
  Transmission details handled by TCP/IP
Notes: Discussion Point
Have students tell you what BIOS stands for.

## Slide 136: Network Protocols
Token ring
  Popular in manufacturing and finance
  Nodes communicate when they have the token

## Slide 137
Network Models
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy
Topics discussed in this section:

## Slide 138
Figure 2.1 Tasks involved in sending a letter

## Slide 139
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:

## Slide 140
ISO is the organization. OSI is the model.
Note

## Slide 141
Figure 2.2 Seven layers of the OSI model

## Slide 142
Figure 2.3 The interaction between layers in the OSI model

## Slide 143
Figure 2.4 An exchange using the OSI model

## Slide 144
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:

## Slide 145
Figure 2.5 Physical layer

## Slide 146
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 147
Figure 2.6 Data link layer

## Slide 148
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 149
Figure 2.7 Hop-to-hop delivery

## Slide 150
Figure 2.8 Network layer

## Slide 151
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 152
Figure 2.9 Source-to-destination delivery

## Slide 153
Figure 2.10 Transport layer

## Slide 154
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 155
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 156
Figure 2.12 Session layer

## Slide 157
The session layer is responsible for dialog control and synchronization.
Note

## Slide 158
Figure 2.13 Presentation layer

## Slide 159
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 160
Figure 2.14 Application layer

## Slide 161
The application layer is responsible for providing services to the user.
Note

## Slide 162
Figure 2.15 Summary of layers

## Slide 163
2-4 TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Physical and Data Link Layers Network Layer Transport Layer
Application Layer
Topics discussed in this section:

## Slide 164
Figure 2.16 TCP/IP and OSI model

## Slide 165
2-5 ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.
Physical Addresses Logical Addresses Port Addresses Specific Addresses
Topics discussed in this section:

## Slide 166
Figure 2.17 Addresses in TCP/IP

## Slide 167
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 168
In Figure 2.19 a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.
Example 2.1

## Slide 169
Figure 2.19 Physical addresses

## Slide 170
Most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2.2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 171
Figure 2.20 shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.
Example 2.3

## Slide 172
Figure 2.20 IP addresses

## Slide 173
Figure 2.21 shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer. Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.
Example 2.4

## Slide 174
Figure 2.21 Port addresses

## Slide 175
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.
Note

## Slide 176
Example 2.5
A port address is a 16-bit address represented by one decimal number as shown.
753
A 16-bit port address represented as one single number.

## Slide 177: Transmission Media
The transmission medium is the physical path by which a message travels from sender to receiver.
Computers and telecommunication devices use signals to represent data.
These signals are transmitted from a device to another in the form of electromagnetic energy.
Examples of Electromagnetic energy include power, radio waves, infrared light, visible light, ultraviolet light, and X and gamma rays.
All these electromagnetic signals constitute the electromagnetic spectrum

## Slide 178
Not all portion of the spectrum are currently usable for telecommunications
Each portion of the spectrum requires a particular transmission medium

## Slide 179
Signals of low frequency (like voice signals) are generally transmitted as current over metal cables. It is not possible to transmit visible light over metal cables, for this class of signals is necessary to use a different media, for example fiber-optic cable.

## Slide 180
Classes of transmission media

## Slide 181: Transmission Media
Guided media, which are those that provide a conduit from one device to another.
Examples: twisted-pair, coaxial cable, optical fiber.
Unguided media (or wireless communication) transport electromagnetic waves without using a physical conductor. Instead, signals are broadcast through air (or, in a few cases, water), and thus are available to anyone who has a device capable of receiving them.

## Slide 182
Guided Media
There are three categories of guided media:
  Twisted-pair cable
  Coaxial cable
  Fiber-optic cable

## Slide 183: Twisted-pair cable
Twisted pair consists of two conductors (normally copper), each with its own plastic insulation, twisted together.
Twisted-pair cable comes in two forms: unshielded and shielded
The twisting helps to reduce the interference (noise) and crosstalk.

## Slide 185
UTP and STP

## Slide 186: Frequency range for twisted-pair cable

## Slide 187: Unshielded Twisted-pair (UTP) cable
Any medium can transmit only a fixed range of frequencies!
UTP cable is the most common type of telecommunication medium in use today.
The range is suitable for transmitting both data and video.
Advantages of UTP are its cost and ease of use. UTP is cheap, flexible, and easy to install.

## Slide 188
The Electronic Industries Association (EIA) has developed standards to grade UTP.
Category 1. The basic twisted-pair cabling used in telephone systems. This level of quality is fine for voice but inadequate for data transmission.
Category 2. This category is suitable for voice and data transmission of up to 2Mbps.
Category 3.This category is suitable for data transmission of up to 10 Mbps. It is now the standard cable for most telephone systems.
Category 4. This category is suitable for data transmission of up to 20 Mbps.
Category 5. This category is suitable for data transmission of up to 100 Mbps.

## Slide 189
Table 7.1 Categories of unshielded twisted-pair cables
Category | Bandwidth | Data Rate | Digital/Analog | Use
1 | very low | < 100 kbps | Analog | Telephone
2 | < 2 MHz | 2 Mbps | Analog/digital | T-1 lines
3 | 16 MHz | 10 Mbps | Digital | LANs
4 | 20 MHz | 20 Mbps | Digital | LANs
5 | 100 MHz | 100 Mbps | Digital | LANs
6 (draft) | 200 MHz | 200 Mbps | Digital | LANs
7 (draft) | 600 MHz | 600 Mbps | Digital | LANs

## Slide 190
UTP connectors
The most common UTP connector is RJ45 (RJ stands for Registered Jack).

## Slide 191: Shielded Twisted (STP) Cable
STP cable has a metal foil or braided-mesh covering that enhances each pair of insulated conductors.
The metal casing prevents the penetration of electromagnetic noise.
Materials and manufacturing requirements make STP more expensive than UTP but less susceptible to noise.

## Slide 192: Applications
Twisted-pair cables are used in telephones lines to provide voice and data channels.
The DSL lines that are used by the telephone companies to provide high data rate connections also use the high-bandwidth capability of unshielded twisted-pair cables.
Local area networks, such as 10Base-T and 100Base-T, also used UTP cables.

## Slide 193: Coaxial Cable (or coax)
Coaxial cable carries signals of higher frequency ranges than twisted-pair cable.
Coaxial Cable standards:
RG-8, RG-9, RG-11 are
used in thick Ethernet
RG-58 Used in thin Ethernet
RG-59 Used for TV

## Slide 194
BNC connectors
To connect coaxial cable to devices, it is necessary to use
coaxial connectors. The most common type of connector is the Bayone-Neill-Concelman, or BNC, connectors. There are three
types: the BNC connector, the BNC T connector, the BNC terminator.
Applications include cable TV networks, and some traditional Ethernet LANs like 10Base-2, or 10-Base5.

## Slide 195: Optical Fiber
Metal cables transmit signals in the form of electric current.
Optical fiber is made of glass or plastic and transmits signals in the form of light.
Light, a form of electromagnetic energy, travels at 300,000 Kilometers/second ( 186,000 miles/second), in a vacuum.
The speed of the light depends on the density of the medium through which it is traveling ( the higher density, the slower the speed).

## Slide 196: The Nature of the Light
Light travels in a straight line as long as it is moving through a single uniform substance.
If a ray of light traveling through one substance suddenly enters another (less or more dense) substance, its speed changes abruptly, causing the ray to change direction. This change is called refraction.

## Slide 197: Refraction

## Slide 198: Critical angle
If the angle of incidence increases, so does the angle of refraction.
The critical angle is defined to be an angle of incidence for which the angle of refraction is 90 degrees.

## Slide 199: Reflection
When the angle of incidence becomes greater than the critical angle, a new phenomenon occurs called reflection.
Light no longer passes into the less dense medium at all.

## Slide 200
Critical Angle

## Slide 201
Optical fibers use reflection to guide light through a channel.
A glass or core is surrounded by a cladding of less dense glass or plastic. The difference in density of the two materials must be such that a beam of light moving through the core is reflected off the cladding instead of being into it.
Information is encoded onto a beam of light as a series of on-off flashes that represent 1 and 0 bits.

## Slide 202
Fiber construction

## Slide 203: Types of Optical Fiber
There are two basic types of fiber: multimode fiber and single-mode fiber.
Multimode fiber is best designed for short transmission distances, and is suited for use in LAN systems and video surveillance.
Single-mode fiber is best designed for longer transmission distances, making it suitable for long-distance telephony and multichannel television broadcast systems.

## Slide 204: Propagation Modes (Types of Optical Fiber )
Current technology supports two modes for propagating light along optical channels, each requiring fiber with different physical characteristics: Multimode
and Single Mode.
Multimode, in turn, can be implemented in two forms: step-index or graded index.

## Slide 205
Multimode: In this case multiple beams from a light source move through the core in different paths.
In multimode step-index fiber, the density of the core remains constant from the center to the edges. A beam of light moves through this constant density in a straight line until it reaches the interface of the core and cladding. At the interface there is an abrupt change to a lower density that alters the angle of the beam’s motion.
In a multimode graded-index fiber the density is highest at the center of the core and decreases gradually to its lowest at the edge.

## Slide 206
Propagation Modes

## Slide 207
Single mode uses step-index fiber and a highly focused source of light that limits beams to a small range of angles, all close to the horizontal.
Fiber Sizes
Optical fibers are defined by the ratio of the diameter of their core to the diameter of their cladding, both expressed in microns (micrometers)
Type | Core | Cladding | Mode
50/125 | 50 | 125 | Multimode, graded-index
62.5/125 | 62.5 | 125 | Multimode, graded-index
100/125 | 100 | 125 | Multimode, graded-index
7/125 | 7 | 125 | Single-mode

## Slide 208
Light sources for optical fibers
The purpose of fiber-optic cable is to contain and direct a beam of light from source to target.
The sending device must be equipped with a light source and the receiving device with photosensitive cell (called a photodiode) capable of translating the received light into an electrical signal.
The light source can be either a light-emitting diode (LED) or an injection laser diode.

## Slide 209
Fiber-optic cable connectors
The subscriber channel (SC) connector is used in cable TV. It uses a push/pull locking system. The straight-tip (ST) connector is used for connecting cable to networking devices. MT-RJ is a new connector with the same size as RJ45.

## Slide 210: Advantages of Optical Fiber
The major advantages offered by fiber-optic cable over twisted-pair and coaxial cable are noise resistance, less signal attenuation, and higher bandwidth.
Noise Resistance: Because fiber-optic transmission uses light rather than electricity, noise is not a factor. External light, the only possible interference, is blocked from the channel by the outer jacket.

## Slide 211: Advantages of Optical Fiber
Less signal attenuation
Fiber-optic transmission distance is significantly greater than that of other guided media. A signal can run for miles without requiring regeneration.
Higher bandwidth
Currently, data rates and bandwidth utilization over fiber-optic cable are limited not by the medium but by the signal generation and reception technology available.

## Slide 212: Disadvantages of Optical Fiber
The main disadvantages of fiber optics are cost, installation/maintenance, and fragility.
Cost. Fiber-optic cable is expensive. Also, a laser light source can cost thousands of dollars, compared to hundreds of dollars for electrical signal generators.
Installation/maintenance
Fragility. Glass fiber is more easily broken than wire, making it less useful for applications where hardware portability is required.

## Slide 213: Unguided Media
Unguided media, or wireless communication, transport electromagnetic waves without using a physical conductor. Instead the signals are broadcast though air or water, and thus are available to anyone who has a device capable of receiving them.
The section of the electromagnetic spectrum defined as radio communication is divided into eight ranges, called bands, each regulated by government authorities.

## Slide 215: Propagation of Radio Waves
Radio technology considers the earth as surrounded by two layers of atmosphere: the troposphere and the ionosphere.
The troposphere is the portion of the atmosphere extending outward approximately 30 miles from the earth's surface.
The troposphere contains what we generally think of as air. Clouds, wind, temperature variations, and weather in general occur in the troposphere.
The ionosphere is the layer of the atmosphere above the troposphere but below space.

## Slide 216
Propagation methods

## Slide 217
Ground propagation. In ground propagation, radio waves travel through the lowest portion of the atmosphere, hugging the earth. These low-frequency signals emanate in all directions from the transmitting antenna and follow the curvature of the planet. The distance depends on the power in the signal.
In Sky propagation, higher-frequency radio waves radiate upward into the ionosphere where they are reflected back to earth. This type of transmission allows for greater distances with lower power output.
In Line-of-Sight Propagation, very high frequency signals are transmitted in straight lines directly from antenna to antenna.

## Slide 218
Bands
Band | Range | Propagation | Application
VLF | 3–30 KHz | Ground | Long-range radio navigation
LF | 30–300 KHz | Ground | Radio beacons and navigational locators
MF | 300 KHz–3 MHz | Sky | AM radio
HF | 3–30 MHz | Sky | Citizens band (CB), ship/aircraft communication
VHF | 30–300 MHz | Sky and line-of-sight | VHF TV, FM radio
UHF | 300 MHz–3 GHz | Line-of-sight | UHF TV, cellular phones, paging, satellite
SHF | 3–30 GHz | Line-of-sight | Satellite communication
EHF | 30–300 GHz | Line-of-sight | Long-range radio navigation

## Slide 219: Propagation of Specific Signals
VLF Very Low Frequency waves are propagated as surface waves, usually through the air but some times through seawater. VLF waves do not suffer much attenuation in transmission but are susceptible to the high levels of atmospheric noise ( heat and electricity) active at low altitudes.
VLF waves are use mostly for long-range radio navigation and for submarine communication.

## Slide 220
LF low frequency waves are also propagated as surface waves. LF waves are used for long-range radio navigation and for radio beacons or navigational locators.
MF Middle frequency signals are propagated in the troposphere. Uses for MF transmissions include AM radio, maritime radio, and emergency frequencies.

## Slide 221
HF high frequency signals use ionospheric propagation. These frequencies move into the ionosphere, where they are reflected back to earth. Uses for HF signals include amateur radio, citizen’s band (CB) radio, military communication, long-distance aircraft and ship communication, telephone, telegraph, and fax.

## Slide 222
VHF Most very high frequency waves use line-of-sight propagation. Uses for VHF include VHF television, FM radio, and aircraft navigational aid.
UHF Ultrahigh frequency waves always use line-of-sight propagation. Uses for UHF includes UHF television, mobile telephone, cellular radio, and microwave links.

## Slide 223
SHF Superhigh frequency waves are transmitted using mostly line-of-sight and some space propagation. Uses for SHF include terrestrial and satellite microwave and radar communication.
EHF Extremely high frequency waves use space propagation. Uses for EHF are predominantly scientific and include radar, satellite and experimental communications.